A damn good ISA (ADG 2)
# Registers
16 General purpose registers, one hardwired to zero.
One global pointer register (R16) – general purpose width
16 Floating point registers, none hardwired
Registers have 64 data bit + 1 “pointer” bit + 3 extra address space bits/flag bits
Extra bits used in FPU for extra range of floating point values, no proper support for denormals except by means of exceptions
Pointer layout:
21 bits+ 1 extra bit for pointer indicator.
Lowest 5 bits, exponent, reverse order
Low bound 8 bits
Upper bound 8 bits
The 8-th bit (bit 7) of each bound copies the corresponding bit from the “upper” bits rather than specify the bound.
This is to allow to determine if we are on upper or lower bound.
If a pointer gets out of exponent range then, depending on the sec flag an exception is triggered (1) or nothing is done.
Maximum pointer range 43 bits.
Minimum allocation 32 bytes.
8 Separate address spaces
R14 and R15 can be used as flag registers.
In some implementations, taking a jump or executing a system instruction might clear the extra flag bits or leave them undefined.
However, the operating system shouldn’t erase them on interrupt or context switch.
# Basic instruction encoding:

## Load/Store:

Base + Index*8 + Signed offset (14 bit).

6 bit opcode.

Datum Source / Target Register is included aswell, in the second position.
Second source register is in the third position.
If base register is R0 (zero hardwired register) then R16 (global pointer) is used instead.

## Immediate ALU:

One source register, one target register, 16 bit immediate (unsigned)
8 bit opcode
operations supported:
add64
sub64
add32s
sub32s
add32z
sub32z
and
or
xor
BIC (immediate inverted).
Mov immediate (source register extends immediate, 20 bits signed)
Mov immediate (source register extends immediate, 20 bits signed shl 12)
add64/u
sub64/u
add32s/u
sub32s/u
add32z/u
sub32z/u
and /u
or/u
xor/u
BIC (immediate inverted)./u
u means upper 16 bits
add64/xu
add64/xxu
setu64/xxxu
compare64 (target register=flag register; has C and O flags in the extra address space bits)
compare32(target register=flag register; has C and O flags in the extra address space bits)
deposit_sans_shift (source register same as target register, “source register” lower 3 bits=byte offset of the immediate, 4-th bit=shift register immediate indicator instead of DSS
xu=third 16 bit piece
xxu=fourth 16 bit piece
xxxu=upper 4 bits set
total 25 uses up 7 6-bit opcode values
Two first bit of the second source register = extra opcode bits.
## Shift instructions

8 bit fixed opcode, 4 bit target register, 4 bit field {1,shift_kind_3},4 bit first(!) source register, 8 bits for shift amount (up to 6 used), 4 bits=extra opcode, should be zero for shift insns, non zero for extra immediate instructions. Extra opcode 1 is used for register-register shift, in which case the second source register is taken from the lower 4 bits of the immediate field.
## Branch instructions
### Compare and Jump registers
2 source registers, 16 condition codes (DS/T pos), Jump target 12 bit signed shl 1
### Compare and Jump with immediate
1 source register, 12 bit signed immediate, 16 condition codes (lowest 2 bits in opcode lowest bits of it), Jump target 8 bit signed shl 1
Total 10 6 bit opcodes 32/64 32i/64i
### Jump and link
26 bit signed immediate shl 6 (Jump taget)
Target register for link: register number 5
### Jump Unconditional
26 bit signed immediate (Jump taget)
### Jump Unconditional aligned
26 bit signed immediate shl 5 (Jump taget)
Total 3 opcodes
# Three operand operates
3 registers, 12 bit opcode.
2 registers, 16 bit opcode
1 register, 5 bit SYSTEM opcode, 15 bit system register (used bits impl. Dependent), can be offset sometimes
total 1 6 bit opcode

1 spare opcode
7+10+3+2=22 opcodes used for non-load/store operations
So up to 21 Loads and 21 Stores
# 16 bit instructions
The 16 bit instruction use is indicated by an extra bit of the 64 bits of data, one per 16 bit instruction.
The extra bits are used as instruction “stop” bits.
So far, only 32 and 16 bit instructions are supported
## Conditional jump instructions
4 bit opcode, 4 bit condition, 8 bit immediate (signed, shl 1)
= 2 4 bit opcodes (R15,R14 flags)
## Immediate ALU
4 bit opcode, 4 bit register, 8 bit immediate (signed)
add64
add32s
add32z
and
or
xor
Mov immediate
## ALU/FPU
8 bit opcode, 4 bit source register, 4 bit target register
(total up to 112 instructions)
Alternative encoding for RET/LINK/INDIR_JMP:
7 bit opcode, 5 bit jump offset (signed, shl 1, link only), 4 bit target/source register

# OPCODE LISTINGS
## Integer load/store:
(bit 0 = store)
0/1 = byte zx
2/3 = two byte zx
4/5 = four byte zx
6/7 = eight bytes + 4 bits
8/9 = byte sx into 4 bytes
10/11 = two byte sx into 4 bytes
12/13 = four byte sx into 8 bytes
14/15 = 9 byte fill/spill (used to guaranteed saving of extra flag bits, even when not implemented in memory).
## Floating point Load/Store:
16/17 = double
18/19 = single
20/21 = single into double
22/23 = double into single
24/25 = double, guaranteed no use of extra bits
26/27 = single, guaranteed no use of extra bits
## Vector load/store
28//29 = single, vector wide (width implementation dependant)
30/31 = integer, vector wide (width implementation dependant, can be different from single)
32/33 = double, vector wide (width implementation dependant, might be single datum)
Conversions between domains produce an unknown result for the vector registers.
34/35 = fill/ spill, implementation dependant, might be odd number of bytes or at least non power of 2.
## Special load/stores
36/37 = extended to extended
38/39 = Extended ↔ Double
40/41 = Extended ↔ signle
## ALU (imm) opcodes
6 bit opcodes: 42-48, opcode lower 2 bits of the index in lower bits of where rs2 would be
Increasing in the order specified in the text
## Branch opcodes
CJUmp:
49-58, increasing in numbers by the order specified in the text
JAL/JU/JUA
59-61 in that order
reserved: 63
Register-Register: 62
## Register-Register opcodes
### 3 operand
add64
sub64
add32s
sub32s
add32z
sub32z
and
or
xor
7 reserved
faddd
fadds
fsubd
fsubs
fmuld
fmuls
fsqrtd
fsqrts
fdivd
fdivs
fmovd
fmovs
packhld
packlhd
packhhd
packlld
fpaddd
fpadds
fpsubd
fpsubs
fpmuld
fpmuls
fpmovd
fpmovs
packhls
packlhs
packhhs
packlls
4 reserved
padd8
psub8
pand8
por8
pxor8
pandn8
pmov8
1 reserved
padd16
psub16
pand16
por16
pxor16
pandn16
pmov16
1 reserved
### //same code for 16 bit insn reg+reg
4x 2-LUT instructions, instead of rs1 and rs1 it has cond1 and cond2 for r14 and r15. Set to either 1 or zero depending on LUT condition
9x shladd64 instructions
3x rs1=-1 1 2
3x rs2=1 4 8
all combinations, allows 1 cycle multiply up to 9
mul64
mul32
mul64us
mul64uu
mul32us
mul32uu
### 2 operand
movsx 8 32
movsx 8 64
movsx 16 32
movsx 16 64
movsx 32 64
movz 8
movz 16
movz 32
movz 64
mov 64
movp 64
annot64 annotate jump table; sum of register bits = number of 8 byte entries; taken from the next aligned 64 bits after the instruction; works as a unconditional jump
### //same code for 16 bit insn reg+reg, but with 64 added to it
# Optional extensions
## 48 Bit :
Load/store : extra 16 bit offset
Immediate (non u) : extra 16 bit immediate
## MULTIPLY (imm ALU)
opcode 6 bit=reserved (63)
instruction: mul64 mul32 reserved reserved