Heptane CPU Architecture
Copyright © Goran Dakov, 2019

# Memory model:
Between cpu cores, each core doesn’t visibly reorder operations to the same cache-line except putting loads ahead of stores. Within a cache-line, operations are a mix of in-order operations of multiple cores, each core performing the memory operations in order. Loads and stores to different cache lines are not required to have the exact same interleaving. Cache-line flushes are not required between write to code area and its execution, although cache line evictions from the data cache will occur.
Loads and stores to misaligned addresses are allowed. Except some SIMD instructions.
A 65th “pointer” bit is stored per 64 bit memory block. It indicates that the datum is a pointer. If misaligned the lower address 65th bit is used.
Pointer format:
Field	Bits
exponent	63:59
Low bound	52:58
High bound	45:51
Address on low bound	44
Address bits	43:0

Overflows above and underflows below the exponent upper bit +12 generate an exception, except in the following cases:
If low>high and on low, overflow by one allowed
If low>high and not on low, underflow by one allowed. The bounds checking is limited by 7 bits, the lower bits aren’t bound checked. There is a bound instruction to restrict bounds of a pointer.
# Flags register
The flags register has only 6 bits:
C,O,A,S,Z,P
The integer instructions set the flag as in x86.
The floating point compare instructions set the flags in a distinct way
There are lahf/sahf instructions which load and store the flag in the lowest 8 bits of a register. Upper bits are zeroed on lahf.
Shifts of zero shift count do not preserve the flags register, but set it according to result, carry=0, overflow=0.
Floating point compare:
AF,OF cleared
Condition	Flags
Unordered	ZF=0 CF=0 SF=1 PF=1
Less than	CF=1 ZF=0 SF=1 PF=0
Greater Than	CF=0 ZF=0 SF=0 PF=0
Equals	CF=0 ZF=1 SF=0 PF=0

# General Purpose registers:
There are 32 general purpose registers.
Register number 16 is the special load register, it might not be preserved between a special load and the following instruction.
The registers with numbers 0-15 have lower code density in some cases. Some instructions encodings are limited to the lower 16 registers.

# VLIW-like encoding

Instructions are made out of a number of 16-bit words in a 256-bit bundle. The last 16 bits of the bundle are reserved for stop bits.
Bit 16 of the stop bits is reserved and must be zero. Instructions may not cross bundles. The number of instructions is architecturally limited to 12. The number of branches is architecturally limited to 4. Special register store counts as a branch instruction for the purpose of the limit of 4 branches per bundle. The instructions are sequential i.e. there can be dependencies between them. Unterminated space in the bundle is ignored. Instruction sizes 16,32,48,64,80 bit.

# Load-Store Plus
The Heptane architecture is Load-Store based, except for special load instructions which an implementation might choose to merge with the next instruction when it consumes it. Stores to the spec register by the spec load are not guaranteed to be visible if an exception occurs in the instruction that follows e.g. a FPU instruction. In such case the exception has to be raised with the spec load as the exception’s address.

# Instruction classes:

## General Purpose

ALU:
Instruction	Index
addl	1
subl	3
andl	5
orl	7
xorl	9
addq	0
subq	2
andq	4
orq	6
xorq	8

The 32 bits instructions clear the upper 32-bits.

Shift:
Instruction	Index	Index2
sll	11	43
srl	13	45
sarl	15	44
slq	10	40
srq	12	42
sarq	14	41

The 32 bits instructions clear the upper 32 bits. Note that there are no rotate instructions.

16 bit encodings for shift and alu:
bits 5:1 encode the index
bit 0 encodes immediate version
Shifts only support immediate version in 16-bit encodings
Target register bits 6,11:8
Source register bits 7,15:12
In immediate version the immediate takes the bits of the source register.
In case the instruction is preceded by a “special” load instruction, the following modifications happen:
if not immediate, bits 6,11:8 indicate first source register, and the second source register is r16
if immediate, the first source register is r16

32 bit ALU encoding:
bits 7:3,1 encode index
bit 2 is zero

bit 0 encodes immediate encoding
bit 31 encodes “flag-less” operation, if set flags are not affected
immediate is in bits 30:18, sign extended
first source 17,11:8
target 16:12
Non immediate:
second source 22:18, bits 30:23 clear
For the shift instructions, Index2 is used for bits 7:0
bit 30 indicates immediate
registers are same
immediate is in bits 23-18
bit 24 indicates flag-less operation
bits 31,29:25 are zero

48-bit alu instructions (immediate):
bits 47:16 are a 32 bit immediate
first source register 11:8
target register 15:12
only the lower 16 registers are accepted.

64-bit alu instructions:

first source register 48,11:8
target register 49,15:12

bits 63:50 zero (unchecked)

Multiplier instructions:
Instruction	Index
imull	4
imulq	6
imullq	5
limulq	7
mull	0
mulq	2
mullq	1
lmulq	3
Ptr bound enptr	8
Ptr bound unptr	9

no 16-bit encodings

Index bits 7:3,1
bit 2 is one
bit 0 is immediate
32 bit encoding, immediate 31:18 sign extended
first source 17,11:8
target 16:12
Non immediate:
second source 22:18, bits 30:23 clear
48-bit alu instructions (immediate):
bits 47:16 are a 32 bit immediate
first source register 11:8
target register 15:12
only the lower 16 registers are accepted.

64-bit alu instructions:

first source register 48,11:8
target register 49,15:12

bits 63:50 zero (unchecked)

Compare and Test instructions

Instruction	imm	Index	Index2
cmpq		2	46
cmpq	yes	3	47
cmpl		4	48
cmpl	yes	5	49
testl		6	52
testq		7	50
testl	yes		53
testq	yes		51

16 bit encoding:
bits 5:3=101
bits 2:0=index
first source bits 17,15:12
second source bits 16,11:8
immediate bits 16,11:8

32 bit encoding:
Index2 in bits 7:0
immediate operand if bit 31
non immediate:
first source: bits 16:12
second source: bits 17,11:8
immediate:
immediate 31:18 sign extended

48 bit encoding: always immediate
first source bits 12:8
immediate 47:32

Compare-jump combination instructions
Jump type	Index
Equal	0
Non-Equal	1
Sign	2
Not Sign	3
Unsigned Greater Than	4
Unsigned Less or Equal	5
Unsigned Greater Than or Equal	6
Unsigned Less Than	7
Signed Greater Than	8
Signed Less or Equal	9
Signed Greater Than or Equal	10
Signed Less Than	11
Overflow	12
Not Overflow	13
Parity	14
Not Parity	15

No 16 bit instructions
Bit 0=32 bit if set; 64 bit otherwise
jump type:
a) 32 bit insn – bits 18,3:1
b) >32 bit insn – bits 32,3:1
bits 7:4=1010
source register 1: bits 17,11:8
source register 2: bits 16,15:12

for 32 bit instruction, it is always register-register
offset at bits 31:18 in multiple of 2
for >32 bit, offset max_bit:33 in multiple of 2
for >32 bit, bit 18=immediate in bits 31:19, signed ( source register 2 must be zero)

Self test compare and jump:
jump type 11:8
register 16:12
bits 7:0=179 32 bit and, 178 64 bit and
32 bit insn: offset bits 31:18 x2, bit 17 zero
48 bit insn: offset bits 47:33 x2

Jump instructions:

16 bit instructions
bits 5:2=1100
bits 7,6,1,0=index (except 15=unconditional)
bits 15:8 signed offset x2

Conditional jump, >=32 bit: 180
jump index: bits 11:8
offset 32 bit: bits 31:12 x2
offset 48 bit: bits 47:17 x2

Unconditional jump, >=32 bits 181
offset 32 bits: bits 31:8 x2
offset 48 bits : bits 47:17 x2

Indirect jump, 32 bit: 182
register bits 12:8
bits 15:13=0

Call and ret

link return address:
16 bit:
target register: 1, bits 11:8
offset bits 15:12 x2 (return address)
bits 7:0=11011000
32 bit:
target register bits 12:8
offset bits 31:16 x2 (return address)
bits 7:0=199

Call subroutine:
either a jump after a link, or a call instruction, which stores the address at the stack top. The stack pointer is not incremented.
Bits 7:0=182
bits 15:13=1 or 2 (decimal)
register bits 12:8
offset (32 bits) 31:16 x2
offset (48 bits) 47:17 x2

Return from subroutine
bits 7:0 182
bits 15:13=11 (3 decimal)
bits 12:8=register
bits 31:15=reserved (unchecked)

Move / sign and zero extend

Instruction	Index	Index2
movq	32, 41(imm)	183
movl	33	184
movw		185
movb		186
movzbq	34	187
movzwq	35	188
movsbl	36	189
movsbq	38	191
movswl	37	190
movswq	39	192
movslq	40	193

16 bit move/extend
bits 5:0=Index
bits 7,15:12=target register
bits 6,11:8=source register/immediate

>=32 bit move/extend
bits 7:0=index2
32 bit insn: source register 16,15:12
        destination register 17,11:8
        imm=bit 31
        immediate value=bits 30:18
48 bit insn: destination register 12:8 (imm only)
        immediate bits 47:16
80 bit insn: destination register 12:8
        immediate bits 79:16

for mov8, bit 30=source high, bit 29=dest high

Conditional set

Conditional set, zeroes the upper 56 bits rather than preserve them.
32 bit format only
bits 17,11:8 target register
bits 15:12 = jump index2

Conditional Move

32 bit instruction only

bits 7:0=198 (decimal)
bits 31:29=000
first source register=bits 17,11:8
second source register=bits 22:18
target register=bits 16:12
jump index=bits 25:23,26
bits 28:27=0 reg to flags,1 64 bit, 2 32 bit, 3 move uncond. reg to/from flag
the unconditional move has 0 in bit 26 if it is reg→flag, 1 if flag→reg .
movbf/movfb

## Load / Store Instructions
Load instructions
Load instruction	Index	SIMD/FPU
Inv tlb	5	N
Prefetch	4	N
64 bit gen purp	3	N
32 bit gen purp (ZX)	2	N
16 bit gen purp (ZX)	1	N
8 bit gen purp (ZX)	0	N
128 bit int (u)	0	Y
128 bit double (u)	1	Y
128 bit single (u)	2	Y
128 bit int (a)	12	Y
128 bit double (a)	13	Y
128 bit single (a)	14	Y
Extended 80-bit	3	Y
Single-to-Extended	4	Y
Single-to-single	5	Y
Single-to-double	6	Y
double-to-extended	8	Y
double-to-double	9	Y
Single pair-to-double pair	10	Y
64 bit int (u)	7	Y
160 bit fill/spill	15	Y
single-pair-to-single-pair	11	Y

Load Base + Offset

bits 7:0=64+Index*2 + (~FPU)*32

32 bit: bits 17,11:8=base
32 bit: bits 16:12=target register
32 bit: offset=bits 31:18

48 bit: bits 15:12=base
48 bit: bits 11:8=lower 4 bits of target
48 bit: upper bit of target is 1 only if SIMD/FPU, except extended target
48 bit: offset=bits 47:16

64 bit: see Base-Index

Base-Index Load

bits 7:0=112 + index*2 + 16*FPU

64 bit: bit 57=base-offset addressing
64 bit: bits 53:52=scale
48 bit: bits 24:23=scale
32 bit: bits 22:21=scale
64 bit: bit 58=no base
64 bit: bit 59=IP relative (requires no base)
64 bit: bits 63:60=0000
64 bit: offset=bits 47:16
48 bit: offset=bits 47:25
32 bit: offset=bits 31:23
64 bit: target reg=bits 54,11:8
64 bit: base=bits 55,15:12
64 bit: index=bits 56,51:48
48 bit: target=bits 20,11:8
48 bit: base=bits 21,15:12
48 bit: index=bits 22,19:16
32 bit: target=bits 20,11:8
32 bit: base=bits 15:12
32 bit: index=bits 19:16

Global variable load

FPU: bits 7:0=60+2*IPRel
~FPU: bits 7:0=176+
FPU: bits 11:8=index
~FPU: bits 10:8=index
~FPU: bit 11=IPRel

32 bit: target 16:12
32 bit: bit 17=0
32 bit: offset 31:18
48 bit: target lower 4 bits 15:12
48 bit: if FPU non extended upper bit one
48 bit: if target=RSP replace with r16; change to spec load
48 bit: offset 47:16

IP relative jumps relative to the 16-bit word after the instruction

Load Base and Offset (SPEC)

FPU: bits 7:0=54
~FPU: bits 7:0=202

bits 11:8=index
~FPU: target=r16
FPU: target =#15 (xmm31/f15)

32 bit: base=bits 16:12
32 bit: offset=31:18
48 bit: base=bits 15:12
48 bit: offset bits 47:16
64 bit: see Base Index Load (SPEC)

Load Base-Index (SPEC)

~FPU: bits 7:0=203
FPU: bits 7:0=55
64 bit: bit 57=base-offset
64 bit: bit 59=IP relative (requires bit 58=no base)
64 bit: scale=bits 53:52
48 bit: scale=bits 24:23
32 bit: scale=bits 22:21
64 bit: bits 58=no base
64 bit: offset=bits 47:16
48 bit: offset=bits 47:25
32 bit: offset=bits 31:23
64 bit: base=bits 55,15:12
64 bit: index=bits 56,51:48
48 bit: base=bits 21,15:12
48 bit: index=bits 22,19:16
32 bit: base=bits 15:12
32 bit: index=bits 19:16

Store instructions
Note floating point instructions that reduce precision do so with “truncate” rounding. Use explicit round instructions if you need other rounding modes.

Store instruction	Index	FPU/SIMD
64 bit int	3	N
32 bit int	2	N
16 bit int	1	N
8 bit int	0	N
Int 128 bit(u)	10	Y
Double 128bit(u)	11	Y
Single 128bit(u)	12	Y
Int 128 bit(a)	0	Y
Double 128bit(a)	1	Y
Single 128bit(a)	2	Y
extended->extended	3	Y
extended->double	4	Y
extended->singe	6	Y
double->double	5	Y
double->single	7	Y
single->single	8	Y
Single pair(single)	13	Y
Int 64	9	Y
spill/fill	15	Y

Store Base+Offset

bits 7:0=64+Index*2 + (~FPU)*32+1

32 bit: bits 17,11:8=base
32 bit: bits 16:12=data register
32 bit: offset=bits 31:18

48 bit: bits 15:12=base
48 bit: bits 11:8=lower 4 bits of data reg
48 bit: upper bit of data reg is 1 only if SIMD/FPU, except extended source
48 bit: offset=bits 47:16
48 bit, non FPU target RSP→changed to R16

64 bit: see Base-Index

Store Base-Index

bits 7:0=112 + index*2 + 16*FPU+1

64 bit: bit 57=base-offset addressing
64 bit: bits 53:52=scale
48 bit: bits 24:23=scale
32 bit: bits 22:21=scale
64 bit: bit 58=no base
64 bit: bit 59=IP relative (requires no base)
64 bit: bits 63:60=0000
64 bit: offset=bits 47:16
48 bit: offset=bits 47:25
32 bit: offset=bits 31:23
64 bit: data reg=bits 54,11:8
64 bit: base=bits 55,15:12
64 bit: index=bits 56,51:48
48 bit: data reg=bits 20,11:8
48 bit: base=bits 21,15:12
48 bit: index=bits 22,19:16
32 bit: data reg=bits 20,11:8
32 bit: base=bits 15:12
32 bit: index=bits 19:16

Store Global

FPU: bits 7:0=61+2*IPRel
~FPU: bits 7:0=177+
FPU: bits 11:8=index
~FPU: bits 10:8=index
~FPU: bit 11=IPRel

32 bit: data reg 16:12
32 bit: bit 17=0
32 bit: offset 31:18
48 bit: data reg lower 4 bits 15:12
48 bit: if FPU non extended upper bit of data reg is one
48 bit: offset 47:16

## Integer SIMD instructions
SIMD ALU
Size code	Index
64	3
32	2
16	1
8	0
Instruction	Index	size	index2
pxor	1	0	2
por	1	1	1
pand	1	2	0
pnot	1	3	7
pmov			3
pandn			4
pnor			5
pnxor			6
add	2	size	0
sub	2	size	1
Add (s)			2
Sub (s)			3
Add (u)			4
Sub (u)			5
Min (s)			6
Max (s)			7
Min (u)			8
Max (u)			9
slp		0,1	2
srp		0,1	0
sarp		0,1	1

16 bit instructions:
bits 5:0=24+index*2+0
bits 7:6=size
if not following a spec load:
target reg lower=bits 11:8
target reg upper=1
source reg lower=bits 15:12
source reg upper=1
if after spec load:
target reg same
first source reg lower=bits 15:12
first source reg upper=1
second source reg=#15 (xmm31)

32 bit instructions

bits 7:0=200
first source register=bits 21:17
second source register=bits 26:22
target register=bits 31:27

add sub (saturated including) min max
size=bits 15:14
index2=bits 13:8
bit 16=0
compare
size=bits 15:14
bits 13:12=01
jump index=bits 11:8
bit 16=0
bitwise
bits 13:9=5
bits 15:14=lower 2 bits of index2
bit 8=upper bit of index2
bit 16=0
first source register is zero in the cases of not and mov.
Untyped mov
bits 13:8=3
bit 16=1
copies the type of the xmm register, usable on single and double as well with no domain crossing cost
Shift
bits 13:8=index2
bit 16=1
bit 15=0
bit 14=size (8 or 16 bit)

## Floating Point instructions

Instruction	index	index2
fadddh	116	0
fadddl	52	1
fadddp	60	6
fsubdh	118	2
fsubdl	54	3
fsubdp	62	7
fmuldh	120	4
fmuldl	56	5
fmuldp	58	8
faddsubdp		9
fadde	1	22
fadds	1	16
faddsp	5	19
fsube	2	23
frsube	3
fsubs	2	17
fsubsp	6	20
fmule	0	24
fmuls	0	18
fmulsp	4	21
fsqrtdh		32
fsqrtdl		33
fsqrte		36
fsqrts		38
fdivdh		34
fdivdl		35
fdive		37
fdivs		39
fperm		26
fandp		40
forp		41
fxorp		42
fandnp		43
fcmplt{s/d}p		32
fcmpge{s/d}p		33
fcmpeq{s/d}p		34
fcmpne{s/d}p		35
Verbatim double to gen		40
Double to gen64		41
Double to gen32		42
Single to gen64		44
Single to gen32		45
Extended to gen64		43
Integer to double		41
Integer to single		42
Integer to Extended		40
fcmpdh		32
fcmpdl		33
fcmpe		34
fcmps		35
frndes		36
frnded		37
frndds		38

## Double-like Precision
Format:
- bits 52:33,31:0=significant
- bit 32=ignored
- bit 64=sign
- bits 65,63:53=exponent
- zero exponent=zero value (no denormals)
- all ones exponent=NaN
- all but bit zero of exponent set: infinity
- bits 67:66=data type

16 bit (double non-packed):
cross-over=1 bit
bits 6:0=index + cross-over
no spec load:
target register low bits=bits 11:8
target register upper bit=1
source register=bits 7,15:12
following spec load
target register low bits=bits 11:8
target register upper bit=1
first source register=bits 7,15:12
second source register=#15 (xmm31)

16 bit (double packed):
cross-over=2 bit
bits 6:0=index + cross-over[0] + cross-over[1]*64
if both cross over, and instruction is add or sub, enable operand pre swapping on high order bits
no spec load:
target register low bits=bits 11:8
target register upper bit=1
source register=bits 7,15:12
following spec load
target register low bits=bits 11:8
target register upper bit=1
first source register=bits 7,15:12
second source register=#15 (xmm31)

32 bit (double,add/mul/sub/addsub)
bits 7:0=240
bits 13:8=index2
bit 16=pre swap high half (zero for multiplication)
bits 15:14=cross-over to other half of second source operand
bits 21:17=first source register
bits 26:22=second source register
bits 31:27=target register

## Single-like precision

Format:
- bits 22:0=significant
- bit 31=sign
- bits 32,30:23=exponent
- zero exponent=zero value (no denormals)
- all ones exponent=NaN
- all but bit zero of exponent set: infinity
data type set per two single-like values rather than one

16-bit instructions (packed/unpacked):
bits 7:6=index[1:0]
bits 5:0=22+2*index[2]
target register lower bits=bits 11:8
source register lower bits=bits 15:12
upper register bits=1

32-bit instructions (add/sub/mul)
bits 7:0=240
bits 13:8=index2
bit 16=alter size (scalar →2x, 4x → 3x)
bits 15:14=cross over (single-like pairs)
bits 21:17=first source register
bits 26:22=second source register
bits 31:27=target register

## Extended-like Precision
Format:
bits 64:33,31:0=significant (inclusive of first one digit)
bit H/15=sign
bits 65,H/14:0=exponent
- zero exponent=zero value (no denormals)
- all ones exponent=NaN
- all but bit zero of exponent set: infinity

16 bit instructions

bits 5:0=20
bits 7:6=index
no spec load:
target reg: 11:8 (reordered?)
source reg: 15:12 (reordered?)

32-bit instructions (add/sub/mul)
bits 7:0=240
bits 13:8=index2
bit 16=0
bits 15:14=0
bits 21:17=first source register (reordered? )
bits 26:22=second source register (reordered ?)
bits 31:27=target register (reordered?)

reordering only happens on the lowest 8 registers.
Reordering bits 7:0=201
Reordering bits 31:8=3 bits per register

## Divide/Square root/logic

32 bit
bits 7:0=240
bits 13:8=index2
bit 16=cross-source for double divide/square root
bit 16=3x single-like datums for logic (single-like only)
bits 15:14=0
bits 21:17=first source register
bits 26:22=second source register
bits 31:27=target register
logic fpu op has auto type between single/double with no domain crossing cost if matching
note that extended precision divide and square root lower 8 registers might be reordered

Packed compare

32 bit
bits 7:0=240
bits 13:8=index2
bits 15:14=2
bit 16=single 1 double 0
bits 21:17=first source register
bits 26:22=second source register
bits 31:27=target register

Compare into flags

32 bit
bits 7:0=240
bits 13:8=index2+4*ordered
bits 15:14=01
bit 16=cross-half source 2

bits 21:17=first source register
bits 26:22=second source register
bits 31:27=target register (must be zero).

Floating point to integer convert

32 bit
bits 7:0=240
bits 13:8=index2
bits 15:14=01
bit 16=cross-half source

bits 21:17=first source register
bits 26:22=second source register
bits 31:27=target register

General purpose to floating point

32 bit
bits 7:0=240
bits 13:8=index2
bits 15:14=2
bit 16=signed

bits 21:17=first source register
bits 26:22=second source register
bits 31:27=target register

Round to lesser precision

32 bit
bits 7:0=240
bits 13:8=index2
bits 15:14=2
bit 16=?

bits 21:17=zeros
bits 26:22=source register
bits 31:27=target register

Logic Instructions

Logic instructions treat infinities as having exponent of all ones and ieee 754 denormals as having exponent of all zeroes.
## System Instructions
Instruction	Index
Write special register	0
Read special register	1
Jump special register	2

No 16 bit versions
32 bit:
bits 7:0=255
bits 31:16=register number
register=bits 12:8 (64 bit)

Write special register does a pipeline stall
Read special register does an issue-breaking point
Jump special register might change from kernel to supervisor mode and vice versa. It is used for systems calls, returns from interrupt, return from kernel mode to user mode.

Special register	Number	Jump
CSR_PAGE	0
CSR_VMPAGE	1
CSR_PAGE0	2
CSR_VMPAGE0	3
CSR_RET_IP	4	Y
CSR_TRAP_RSP_SAVE	5
CSR_TRAP_RSP	6
CSR_PCR	7
CSR_TRAP_TABLE	8
CSR_SAVE_REG	9
CSR_MFLAGS	10
CSR_FPU	11
CSR_SYSCALL	12	Y
CSR_VMCALL	13	Y
CSR_TRANSL_BASE	2
CSR_TRANSL_MASK	14
CSR_TRANSL_INDIR	15
CSR_TRANSL_INDIR_MASK	16
Unbound pointer	17
CSR_CL_LOCK	18
CSR_PTR_COMBINE	32	Y
CSR_PTR_INTERSECT	33	Y
CSR_PTR_RESTR_LOW	34	Y
CSR_PTR_RESTR_UPR	35	Y

Format of CSR_MFLAGS
Name	Bits
Privilege level (0 and 3 valid)	0-1
VM mode	2
Paging	3
IRQ enable	4
EDGE main cpu	5
EDGE helper cpu	6
Double Fault	7
Exception Extra Bits	8-15
Transl_enable	16
Interpret SIMD #15 reg as target reg(ld/st)	17
Cache line locked	18
Allow set pointer bit	19
After spec load	20
Reserved	21-63

Bit 17 is set during type conversion exceptions. A store followed by a load will convert the target register.
If translation is enabled, the virtual address is the concatenation of upper bits, and the lower bits of the virtual address index into the CSR_TRANSL_BASE masked bits. Upper physical bits are the same as the unmasked bits of CSR_TRANSL_BASE. Lower bits ones.

Format of CSR_PAGE, CSR_VMPAGE, CSR_TLB_INV:
upper 24 bits ASID
bits 39:0 address of top level (or invalidated) page, shifted 12 bits

Format of CSR_SPAGE, CSR_ASID_INV:
upper 24 bits shared/invalidated ASID
bits 39:0 ignored

Jump CSR format:
bit 63=supervisor mode
bit 62=In VM
bit 61=After spec load
bits 62:44 zeroes
bits 43:1 target IP
bit 0=zero

CSR_TRAP_TABLE:
bits 63:41=zeroes
bits 40:12=TRAP TABLE virtual adress (64 byte frags x 64 entries)
bits 11:0=zeroes

CSR_TRANSL_BASE:
bits 63:52=zeroes
bits 51:0=physical power 2 aligned base address (determined by CSR_TRANSL_MASK)

CSR_TRANSL_MASK
bits 63:52 zeroes
bits 51:0=mask of all ones for all address bits of the architectural translation segment (contiguous starting from bit 0)

CSR_TRANSL_INDIR:
bits 63:52 zeroes
bits 51:0=Indirect jump cache table power 2 aligned

CSR_TRANSL_INDIR_MASK
bits 63:52 zeroes
bits 51:0=mask of all ones for all address bits of the architectural indirect jump translation cache (contiguous starting from bit 0)

CSR_CL_LOCK:
Address of locked cacheline. On write, locks cl. On read, unlocks it. No automatic insert, only prevents pulling by another core. If on read, zero is returned, that means that the CL was locked by another core. (no writtes committed) Or a time-out occurred (writes may have been comitted). During a locked execution, no IRQs are served.

CSR_FPU bits:
Name	Range
Invalid exception	0
Native underflow	1
IEEE 754 underflow	2
Native overflow	3
IEEE 754 overflow	4
Native inexact	5
IEEE 754 inexact	6
Convert to int SIMD	7
IEEE 754 denormal (requires software handling)	8
Convert to single SIMD	9
Convert to double SIMD	10
Exception has occurred flags	11-21
Rounding mode single/double	22-24
Rounding mode extended precision	25-27
Clip to IEEE range	28
IEEE denormals to zero	29
Reordering indices	40-63

# Page table entry format:
4 Level page table, 64 bit entry, 44 bit virtual address space (first stage selects between *page and *page0)
Name	Bits
No access (inverted)	0
System	1
Write Enable (inverted)	2
Write Through	3
Non cacheable	4
Accessed	5
Dirty	6
Large Page	7
Global Page	8
Write Combine	9
Execute (inverted)	10
Page entry/pointer	13-51 (upper bit varies)
Unused	52-63,11-12

# Indirect branch table format:
The indirect branch table consists of 8-way entry bundles. Each bundle contains 8 128 bit entries. The indirect branch table is generally translated by the tlb. Virtual address upper bits same as translated address, mask 1 bits index into the CSR_TRANSL_BASE. Alignment of the indirect table is 16 bytes of translated address.
Format of the 128 bit entry:
Name	Bits
Virtual Address (translated)	63:0
ASID	87:64
Target address	127:96
Entry enabled	95
Reserved (zeroes)	94:88

# EDGE-like extensions
The reserved bit can be used for an optional Explicit Data graph Execution like architecture. This is achieved by running two cores in write-coalescing mode. A core would need to be able to execute 2 stores per clock cycle. Only one “main” core can execute branches. The “helper” core gets its IP address from the main core. The first instruction bundle needs to have the reserved bit set to one, indicating a bundle pair. The first bundle is sent to the main-core pipeline, and the second bundle is sent to the helper core. The helper core instruction bundle needs to repeat all data stores from the main core, but as special “store external” instructions at the beginning. Those need to be at the beginning of it. The main core needs to have “store external” instructions at its end matching the address of the store instructions of the helper core bundle.
Bits 7:0 (int)	Bits 7:0 (fp)
204	205	Base-Offset
206	207	Base-Index
208	209	Immediate

The format is the same as the corresponding store instructions. The store opcode is in the data register field. The data register is not relevant as the data is forwarded from the other core. The unused bits of the data register field are zero.

# Exceptions / Traps

The exception table consists of 64 64-byte code snippets. If more space is needed, jumps can go elsewhere. The CSR_RET_IP is set to the staring address of the instruction. The extra information bits in CSR_MFLAGS are set. Then a jump to the snippet occurs.
Name	Number
Invalid exception	0
Native underflow	1
IEEE 754 underflow	2
Native overflow	3
IEEE 754 overflow	4
Native inexact	5
IEEE 754 inexact	6
Convert to integer SIMD	7
IEEE 754 denormal (requires software handling)	8
Convert to Single SIMD	9
Convert to double SIMD	10
Page Fault	11
CSR access fault	12
Double Fault	13
IRQ	14
NMI	15
Indirect Branch Table fault	16
Illegal instruction	17

The extra information field in mflags contains the offending register number in case of floating point exception.
In case of Page Fault, bit 0 is read access fault, bit 1 is write access fault, bit 2 is execute access fault, bit 3 is system/user access fault, bit 4 is address security fault. Others are reserved.
In case of CSR access Fault, bit 0 is read access fault, bit 1 is write access fault, bit 2 is execute access fault, bit 3 is vm access fault.
In case of IRQ, it contains the vector number.